## Slide 1: Computer Network (MCA-103) UNIT - I

## Slide 2: Overview
Learning Objective:
  Understand basics, topologies and working mechanism of wired and wireless computer networks.
  Analyze the features and operations of protocols of OSI reference model & TCP/IP protocol suite.
  Design, calculate, and apply routing mechanisms for lPv4 & lPv6.
  ldentify the networking requirements for an organization and select & propose appropriate architecture and technologies.
  Work on Network addressing, design and implementation.

## Slide 3
Overview
UNIT-1
Introductory Concepts:
  Goals and Applications of Computer Networks,
  OSI reference model,
  TCP/lP protocol suite,
  networks topology & design.
  Networking Devices (Hub, Bridge, Switch & router).
  Physical Layer
  Communication Satellites
  Digital Signal Encoding Formats, Digital to analog Modulation
  Digitization - Sampling Theorem, PCM, DM, Analog to digital Modulation
  The Mobile Telephone System
  Multiplexing

## Slide 4
Overview (cont..)
UNIT-2
The Data Link Layer
  Data Link Layer introduction
  Error Detection and Correction,
  Flow Control and Error Control protocols
Medium access sub-layer
  Channel allocation problem
  ALOHA Protocols,
  Carrier Sense Multiple Access Protocols,
  CSMA with Collision Detection,
  Collision free protocols,
  Ethernet, wireless LANs, Blue Tooth, Wi-Fi

## Slide 5
Overview (cont..)
UNIT-3
Network Layer
  Functions of network layer
  lPv4: Classful & classless addressing,
  Routing algorithms, lP packet format
  lPvS: addressing, neighbor discovery, address auto configuration
Mobile lP
  Mobility in networks,
  lP Multicasting (Source based tree & Group shared tree)

## Slide 6
Overview (cont..)
UNIT-4
Transport Layer:
  Transport layer functions
  Transport layer protocols:UDP, TCP
  Connection management, flow control, error control and congestion control.
Application Layer
  DNS, Electronic Mail, www, firewalls
  Concept of public & private keys.

## Slide 7: Unit 1
  In this Unit we will discuss :
  Introduction and The Physical Layer: Uses of Computer Networks, Network Hardware,
  Network Software, Reference Model (OSI, TCP/IP Overview), The Physical Layer,
  Theoretical Basis for Data Communication, Guided Transmission Media, Wireless
  Transmission, Communication Satellites,
  Digital Signal Encoding Formats
  Digital Modulation
  Analog Modulation –The Public Switched Telephone Network, The Mobile Telephone System

## Slide 8: Introduction

## Slide 9: Introduction
Components
Data Representation
Direction of Data Flow
BASICS OF DATA COMMUNICATION

## Slide 10: Introduction
Five components of data communication

## Slide 11: Data Flow
Simplex

## Slide 12: Data Flow
Half-Duplex

## Slide 13: Data Flow
Full-Duplex

## Slide 14: Types of Connection
Point-to-point connection

## Slide 15: Types of Connection
Multi Point Connection

## Slide 16: Introduction
Categories of Topology

## Slide 17: Introduction
MESH (FULLY CONNECTED)

## Slide 18: Introduction
STAR

## Slide 19: Introduction
BUS

## Slide 20: Introduction
RING

## Slide 21: Introduction
Categories of Networks

## Slide 22: Introduction
LAN

## Slide 23: Introduction
LAN

## Slide 24: Introduction
MAN

## Slide 25: Introduction
WAN

## Slide 26: Internet Today

## Slide 27: Network Models

## Slide 28: Internet Layers

## Slide 29: Internet Layers

## Slide 30: Internet Layers

## Slide 31: OSI Model

## Slide 32: Physical Layer
The physical layer is responsible for transmitting individual bits from one node to the next.

## Slide 33: Physical Layer
Responsibilities of Physical Layer :-
Physical Characteristics of interfaces and medium
Representation of bits
Data rate
Synchronization of bits
Line configuration
Physical topology
Transmission mode

## Slide 34: Data Link Layer
The data link layer is responsible for transmitting frames from one node to the next.

## Slide 35: Data Link Layer
Responsibilities of Data Link Layer :-
Framing
Physical Addressing
Flow Control
Error Control
Access Control

## Slide 36: Node to Node Delivery

## Slide 37: Node to Node Delivery
Example
In Figure, a node with physical address 10 sends a frame to a node with physical address 87.
The two nodes are connected by a link. At the data link level this frame contains physical addresses in the header. These are the only addresses needed.
The rest of the header contains other information needed at this level. The trailer usually contains extra bits needed for error detection

## Slide 38: Node to Node Delivery
Example

## Slide 39: Network Layer
The network layer is responsible for the delivery of packets from the original source to the final destination.

## Slide 40: Network Layer
Responsibilities of Network Layer :-
Logical Addressing
Routing

## Slide 41: Source – to - Destination
Notes: Tells the address to and from. Routers are used here for delivery of message

## Slide 42: Source – to - Destination
Example
In Figure, we want to send data from a node with network address A and physical address 10, located on one LAN, to a node with a network address P and physical address 95, located on another LAN.
Because the two devices are located on different networks, we cannot use physical addresses only; the physical addresses only have local jurisdiction.
What we need here are universal addresses that can pass through the LAN boundaries. The network (logical) addresses have this characteristic.

## Slide 43: Source – to - Destination
Example

## Slide 44: Transport Layer
The transport layer is responsible for delivery of a message from one process to another.
Notes: Breaks the data into segments

## Slide 45: Transport Layer
Responsibilities of Transport Layer :-
Service-point addressing
Segmentation and reassembly
Connection control
Flow control
Error Control

## Slide 46: Process to Process

## Slide 47: Process to Process
Example
Figure, shows an example of transport layer communication. Data coming from the upper layers have port addresses j and k (j is the address of the sending process, and k is the address of the receiving process).
Since the data size is larger than the network layer can handle, the data are split into two packets, each packet retaining the port addresses (j and k). Then in the network layer, network addresses (A and P) are added to each packet.

## Slide 48: Process to Process
Example

## Slide 49: Session Layer
The session layer is responsible for dialog control and synchronization.

## Slide 50: Presentation Layer
The presentation layer is responsible for translation, compression, and encryption.

## Slide 51: Application Layer
The application layer is responsible for providing services to the user.

## Slide 52: Application Layer
Services provided by the Application Layer :-
Network virtual terminal
File transfer, access and management
Mail services
Directory services

## Slide 53: Summary of Layers

## Slide 54: OSI Model

## Slide 55: OSI Model

## Slide 56: OSI Model
Physical layer | Deals with the mechanical and electrical specification of the interface and transmission media.
Data Link Layer | Transforms the physical layer, to a reliable link and is responsible for node-to-node delivery.
Network Layer | Responsible for the source-to-destination delivery of a packet across multiple links.

## Slide 57: OSI Model
Transport Layer | Responsible for the source-to-destination (end-to-end) delivery of the entire message.
Session Layer | It establishes, maintains and synchronizes the interaction between communicating systems.
Presentation Layer | It concerns with the syntax and semantics of the information between two systems.

## Slide 58: OSI Model
Application Layer | It provides user interfaces and support for services such as E-Mail, Remote Login and other types of Distributed Information Services.

## Slide 59: Reference Models
The OSI Reference Model
The TCP/IP Reference Model
A Comparison of OSI and TCP/IP
A Critique of the OSI Model and Protocols
A Critique of the TCP/IP Reference Model

## Slide 60: Reference Models
The OSI reference model.

## Slide 61: Reference Models (2)
The TCP/IP reference model.

## Slide 62: Comparing OSI and TCP/IP Models
Concepts central to the OSI model
Services
Interfaces
Protocols

## Slide 63: A Critique of the OSI Model and Protocols
Why OSI did not take over the world
Bad timing
Bad technology
Bad implementations
Bad politics
Disadvantages
Setting up a model is a challenging task.
Sometimes, it becomes difficult to fit a new protocol into this model.
It is only used as a reference model.

## Slide 64: Bad Timing
The apocalypse of the two elephants.

## Slide 65: A Critique of the TCP/IP Reference Model
Problems:
Service, interface, and protocol not distinguished
Not a general model
Host-to-network “layer” not really a layer
No mention of physical and data link layers
Minor protocols deeply entrenched, hard to replace

## Slide 66: Computer Networks
Physical Layer

## Slide 67: Position of Physical Layer

## Slide 68: Physical Layer

## Slide 69
Transmission Media
Physical Layer

## Slide 70
Transmission medium and physical layer
Cont …

## Slide 71
Based on communication channel
Types of network

## Slide 72
Guided: Transmission capacity depends critically on the medium, the length, and whether the medium is point-to-point or multipoint (e.g. LAN). Examples are co-axial cable, twisted pair, and optical fiber.
Unguided: provides a means for transmitting electro-magnetic signals but do not guide them. Example wireless transmission.
Cont …

## Slide 73
Guided Media
Twisted-Pair Cable
Coaxial Cable
Fiber-Optic Cable
Physical Layer

## Slide 74
Physical Layer
A twisted pair consists of two conductors (normally copper), each with its own plastic insulation, twister together
One of the wires is use to carry signals to the receiver, and the other is used only as a ground reference
The receiver uses the difference between the two.
In addition to the signal sent by the sender on one of the wires, interference (noise) and crosstalk may affect both wires and create unwanted signals.
If the two wires are parallel, the effect of these unwanted signals is not the same in both wires because they are at different locations relative to the noise or crosstalk sources.

## Slide 75
Twisted-pair cable
Cont'd…

## Slide 76
UTP and STP
UTP: Unshielded twisted pair cable
STP: shielded twisted pair cable, cable has a metal foil covering that encases each pair of insulated conductors. Electro magnetic noise penetration is prevented by metal casing. Expensive, allow high transmission rate
Cont'd…

## Slide 77
Categories of unshielded twisted-pair cables
Category | Bandwidth | Data Rate | Digital/Analog | Use
1 | very low | < 100 kbps | Analog | Telephone
2 | < 2 MHz | 2 Mbps | Analog/digital | T-1 lines
3 | 16 MHz | 10 Mbps | Digital | LANs
4 | 20 MHz | 20 Mbps | Digital | LANs
5 | 100 MHz | 100 Mbps | Digital | LANs
6 (draft) | 200 MHz | 200 Mbps | Digital | LANs
7 (draft) | 600 MHz | 600 Mbps | Digital | LANs
Cont'd…

## Slide 78
UTP connector
Cont'd…
RJ 45 connector is used with Ethernet cable in computer networking
RJ 11 connector is used in connecting telephone units

## Slide 79
Coaxial cable
Cont'd…
Notes: Eg: used in set top box for cables at home

## Slide 80
Coaxial cable carries signals of higher frequency ranges than those in twisted pair cable, in part because the two media are constructed differently.
Instead of having two wires, coax has a central core conductor of solid or stranded wire (usually copper), enclosed in an insulating sheath , which is, in turn encased in an outer conductor of metal foil.
The outer metallic wrapping serves both as a shield against noise and as the second conductor, which completes the circuit.
This outer conductor is also enclosed in an insulating sheath, and the whole cable is protected by a plastic cover.
Cont'd…

## Slide 81
Categories of coaxial cables
Category | Impedance | Use
RG-59 | 75 W | Cable TV
RG-58 | 50 W | Thin Ethernet
RG-11 | 50 W | Thick Ethernet
RG-Radio Government (ratings)
Cont'd…
Each RG number denotes a unique set of physical specification
Notes: Coaxial cables are categorized by RG ratings

## Slide 82
BNC connectors
BNC – Bayone-Neill-Concelman
Cont'd…

## Slide 83
The BNC connector is used to connect the end of the cable to a device, such as a TV set
BNC T connector is used in ETHERNET
BNC terminator is used at the end of the cable to prevent the reflection of the signal.
Cont'd…

## Slide 84
The attenuation is much higher in coaxial cable that in twister pair.
In other words, although coaxial cable has a much higher bandwidth, the signal weakens rapidly and requires the frequent use of repeaters.
It is less affected by external magnetic field.
Cont'd…

## Slide 85
Optical Fiber is made of glass or plastic and transmit signals in the form of light.
Light travels in a straight line as long as it is moving through a single medium substance.
If a ray of light traveling through one instance suddenly enters another substance (of a different density), the ray changes direction.
Optical Fiber

## Slide 86
Bending of light ray
Cont …

## Slide 87
If the angle of incidence I (the angle the ray makes with the line perpendicular to the interface between the two substance) is less that the critical angle, the ray refracts and moves closer to the surface.
If the angle of incidence is equal to the critical angle, the light bends along the surface.
If the angle I greater than the critical angle, the ray reflects (makes a turn) and travels again in the denser substance.
Note that the critical angle is property of the substance, and its value differs from one substance to another.
Optical Fiber

## Slide 88
Optical fibers use reflection to guide light through a channel.
A glass or plastic is surrounded by a cladding of less dense glass or plastic.
The difference in density of the two materials must be such that a beam of light moving through the core is reflected of the cladding instead of being refracted into it.
Optical Fiber

## Slide 89
Optical fiber
Cont …

## Slide 90
Propagation modes
Cont'd…

## Slide 91
Multimode is so named because multiple beams from a light source move through the core in different paths.
In multimode step-index fiber, the density of the core remains constant from the center to the edges.
A beam of light moves through this constant density in a straight line until it reaches the interface of the core and the cladding.
At the interface, there is an abrupt change due to a lower density, this alters the angle of the beam’s motion.
The term step index refers to the suddenness of this change, which contributes to the distortion of the signal as it passes through the fiber.
Optical Fiber

## Slide 92
Multimode step index fibers are similar to the single mode step index fibers except the center core is much larger with multimode configuration.
With this large core diameter there are many paths through which light can travel.
This type of fiber has a large light to fiber aperture and allows more light to enter the fiber.
The light rays that strike the core/cladding interface at an angle greater than the critical angle are propagated down the core in a zigzag fashion.
Optical Fiber

## Slide 93
Light rays that strike the core/cladding interface at an angle less than the critical angle enter the cladding and are lost.
Light rays take different paths down the fiber, which results in large difference in propagation times.
Due to this light rays travelling down fiber have a tendency to spread out.
Optical Fiber

## Slide 94
Multimode graded-index fiber, decreases this distortion of the signal through the cable.
The word index here refers to the index of refraction.
Refraction is related to the density.
A graded-index fiber, therefore is one with varying densities.
Density is highest at the center of the core and decreases gradually to its lowest at the edge.
Optical Fiber

## Slide 95
The multimode graded index fiber is an improvement on the multimode step index fiber.
Multimode graded index fibers have non-uniform refractive index.
This fiber has maximum density at the center which gradually decreases towards the outer edge.
Light rays propagate down this type of fiber through refraction rather than reflection.
Optical Fiber

## Slide 96
As the light rays propagate down the fiber, the rays travelling in the outer most area of the fiber travel a greater distance than the rays travelling near the center.
Because the refractive index decreases with distance from the center, the light rays travelling farthest from the center propagate at a higher velocity.
Therefore all light rays take approximately the same time to travel the length of the fiber.
Optical Fiber

## Slide 97
Single-mode uses step-index fiber and a highly focused source of light that limits beams to a small range of angles, all close to horizontal.
The single mode fiber itself is manufactures with a much smaller diameter than that of multimode fiber, and with substantially lower density (index of refraction).
Optical Fiber

## Slide 98
Modes
Cont'd…

## Slide 99
Fiber types
Type | Core | Cladding | Mode
50/125 | 50 | 125 | Multimode, graded-index
62.5/125 | 62.5 | 125 | Multimode, graded-index
100/125 | 100 | 125 | Multimode, graded-index
7/125 | 7 | 125 | Single-mode
Cont'd…

## Slide 100
Fiber construction
Cont'd…

## Slide 101
The outer jacket is made of either PVC or Teflon.
Inside the jacket are KEVLAR strands to strengthen the cable.
KEVLAR is a strong material used in the fabrication of bulletproof vests.
Below the KEVLAR is another plastic coating to cushion the fiber.
The fiber is at the center of the cable, and it consists of cladding and core.
Optical Fiber

## Slide 102
Fiber-optic cable connectors
Cont …

## Slide 103
Subscriber Channel (SC) connector is used for cable TV. It used push/pull locking system.
Straight Tip (ST) connector is used for connecting cable to networking devices.
It uses a bayonet locking system and is more reliable than SC.
MT-RJ is a connector that is the same size as RJ45.
Optical Fiber

## Slide 104
Optical fiber performance
Cont'd…

## Slide 105
Unguided transmission is used when running a physical cable (either fiber or copper) between two end points is not possible.
For example, running wires between buildings is probably not legal if the building is separated by a public street.
Infrared signals typically used for short distances (across the street or within same room),
Microwave signals commonly used for longer distances (10's of km). Sender and receiver use some sort of dish antenna
Unguided Media: Wireless
Cont'd…

## Slide 106
Difficulties:
Weather interferes with signals. For instance, clouds, rain, lightning, etc. may adversely affect communication.
2. Radio transmissions easy to tap. A big concern for companies worried about competitors stealing plans.
3. Signals bouncing off of structures may lead to out-of-phase signals that the receiver must filter out.
Unguided Media: Wireless
Cont'd…

## Slide 107
Electromagnetic spectrum for wireless communication
Cont …
Notes: Wireless medium uses electro magnetic waves to transmit. Wavelength is between crust and trough. Higher wavelength less frequency. Higher frequency less wavelength. Higher frequency, higher energy, so as frequency increases it is harmful with more energy.

## Slide 108
Propagation methods
Cont'd…

## Slide 109
Ground propagation – radio waves travel through the lowest portion of the atmosphere.
These low-frequency signals emanate in all directions form the transmitting antenna and follow the curvature of the planet.
Distance depends on the amount of power of the signal : The greater the power, the greater the distance.
WIRELESS

## Slide 110
Sky propagation- higher-frequency radio waves radiate upward into the ionosphere (the layer of atmosphere where particles exists as ions) where they are reflected back to the earth.
This type of transmission allows for greater distances with lower output power.
WIRELESS

## Slide 111
Line –of-Sight propagation - very high-frequency signals are transmitted in straight lines directly from antenna to antenna.
Antennas must be directions, facing each other, and either tall enough or close enough together not to be affected by the curvature of the earth.
WIRELESS

## Slide 112
Bands
Band | Range | Propagation | Application
VLF | 3–30 KHz | Ground | Long-range radio navigation
LF | 30–300 KHz | Ground | Radio beacons and navigational locators
MF | 300 KHz–3 MHz | Sky | AM radio
HF | 3–30 MHz | Sky | Citizens band (CB), ship/aircraft communication
VHF | 30–300 MHz | Sky and line-of-sight | VHF TV, FM radio
UHF | 300 MHz–3 GHz | Line-of-sight | UHF TV, cellular phones, paging, satellite
SHF | 3–30 GHz | Line-of-sight | Satellite communication
EHF | 30–300 GHz | Line-of-sight | Long-range radio navigation
Cont …

## Slide 113
Wireless transmission waves

## Slide 114
Ranges in frequencies between 3 Khz and 1 Ghz.
Radio waves use omnidirectional antenna.
When an antenna transmits radio waves, they are propagated in all directions.
This means that the sending and receiving antenna do not have to be aligned.
A sending antenna send waves that can be received by any receiving antenna.
It has a disadvantage , that radio waves transmitted by one antennas are susceptible to interference by another antenna that may send signals using the same frequency or band.
RADIO WAVE

## Slide 115
Omnidirectional antenna of radio waves make them useful for multicasting, in which there is one sender but many receivers
RADIO WAVE
Notes: Omnidirection: in all directions

## Slide 116
Radio waves are used for multicast communications, such as radio and television, and paging systems. AM, FM, Television, Cordless Phone and paging
Note:
Cont …

## Slide 117
Electromagnetic waves having frequencies between 300 Mhz and 300 GHz are called micro-waves.
It uses uni-directional antenna
When an antenna transmits microwave waves, they can be narrowly focused.
This means that the sending and receiving antennas need to be aligned.
It has an advantage, a pair of antennas can be aligned without interfering with another pair of aligned antennas.
Microwave

## Slide 118
Unidirectional antenna can be parabolic dish antenna and the horn
A parabolic antenna is based on the geometry of a parabola : Every line parallel to the line of symmetry reflects off the curve at angles such that all the lines intersect in a common point called the focus.
The parabolic dish works as a funnel, catching a wide range of waves and directing them to a common point.
In this way, more of the signal is recovered than would be possible with a single-point receiver.
Microwave

## Slide 119
Outgoing transmission are broadcast through a horn aimed at the dish.
The microwaves hit the dish and are deflected outward in a reversal of the receipt path
Outgoing transmission are broadcast up a stem (resembling a handle) and deflected outward in a series of narrow parallel beams of a curved head.
Received transmissions are collected by the scooped shape of the horn, in a manner similar to the parabolic dish, and deflected down into the stem.
USED IN CELLULAR PHONES, SATELLITE NETWORKS, WIRELESS LANs
Microwave

## Slide 120
Unidirectional antennas
Cont …

## Slide 121
Microwaves are used for unicast communication such as cellular telephones, satellite networks, and wireless LANs.
Note:
Cont …

## Slide 122
Infrared signals can be used for short-range communication in a closed area using line-of-sight propagation.
Note:
Cont …

## Slide 123: Satellite Networks
Microwave frequencies, which travel in straight lines, are commonly used for wideband communication.
The curvature of the earth results in obstruction of the signal between two earth stations and the signal also gets attenuated with the distance it traverses.
To overcome both the problems, it is necessary to use a repeater, which can receive a signal from one earth station, amplify it, and retransmit it to another earth station.
Larger the height of a repeater from the surface of the earth, longer is the distance of line-of-sight communication.
Notes: 123

## Slide 124: Satellite Networks
Satellite networks were originally developed to provide long-distance telephone service.
So, for communication over long distances, satellites are a natural choice for use as repeaters in the sky.
Notes: 124

## Slide 125: Satellite Networks

## Slide 126: Satellite Networks

## Slide 127: Satellite Networks
Three different types categories(basis: location of the orbit)
These orbits are chosen such that the satellites are not destroyed by the high-energy charged particles present in the two Van Allen belts,
  The Low Earth Orbit (LEO) is below the lower Van Allen belt in the altitude of 500 to 2000 Km. T
  he Medium Earth Orbit (MEO) is in between the lower Van Allen belt and upper Van Allen belt in the altitude of 5000 to 15000 Km.
  Above the upper Van Allen belt is the Geostationary Earth Orbit (GEO) at the altitude of about 36,000 Km.
Below the Geostationary Earth Orbit and above the upper Van Allen belt is Global Positioning System (GPS) satellites at the altitude of 20,000 Km.
Notes: 127

## Slide 128: Satellite Networks
Notes: 128

## Slide 129: Satellite Networks

## Slide 130: Satellite Networks
Frequency Bands
Two frequencies are necessary for communication between a ground station and a satellite; one for communication from the ground station on the earth to the satellite called uplink frequency and another frequency for communication from the satellite to a station on the earth, called downlink frequency.
These frequencies, reserved for satellite communication, are divided in several bands such as L, S, Ku, etc are in the gigahertz (microwave) frequency range as shown in Table . Higher the frequency, higher is the available bandwidth.
Notes: 130

## Slide 131: Satellite Networks
Band | Downlink, GHz | Uplink, GHz | Bandwidth, MHz
L | 1.5 | 1.6 | 15
S | 1.9 | 2.2 | 70
C | 4 | 6 | 500
Ku | 11 | 14 | 500
Ka | 20 | 30 | 3500
Satellite frequency band

## Slide 132: Satellite Networks
LEO satellite system

## Slide 133: Satellite Networks
Iridium constellation
The Iridium system has 66 satellites in six LEO orbits, each at an altitude of 750 km.

## Slide 134: Satellite Networks
GPS
Medium Earth Orbit
Notes: 134

## Slide 135: Satellite Networks
GPS
The Global Positioning System (GPS) is a satellite-based navigation system. It comprises a network of 24 satellites at an altitude of 20,000 Km (Period 12 Hrs) and an inclination of 55° as shown in Fig.
Originally intended for military applications and deployed by the Department of Defence, the system is available for civilian use since 1980.
Allows land, sea and airborne users to measure their position, velocity and time.
Works in any weather conditions, 24 hrs a day.
Positioning is accurate to within 15 meters.
Notes: 135

## Slide 136: Physical Layer
Signals

## Slide 137: Physical Layer
To be transmitted, data must be transformed to electromagnetic signals.

## Slide 138: Physical Layer
Signals can be analog or digital. Analog signals can have an infinite number of values in a range; digital signals can have only a limited number of values.

## Slide 139: Physical Layer
Comparison of analog and digital signals

## Slide 140: Analog Signals
Sine Wave
Phase
Examples of Sine Waves
Time and Frequency Domains
Composite Signals
Bandwidth

## Slide 141: Sine Wave

## Slide 142: Amplitude

## Slide 143: Signals
Frequency is the rate of change with respect to time. Change in a short span of time means high frequency. Change over a long span of time means low frequency.

## Slide 144: Signals
If a signal does not change at all, its frequency is zero. If a signal changes instantaneously, its frequency is infinite.

## Slide 145: Signals

## Slide 146: Signals
The bandwidth is a property of a medium: It is the difference between the highest and the lowest frequencies that the medium can satisfactorily pass.

## Slide 147: Signals
Here, we use the term bandwidth to refer to the property of a medium or the width of a single spectrum.

## Slide 148: Bandwidth

## Slide 149: Example

## Slide 150: Digital Versus Analog

## Slide 151: Transmission Impairment
A transmission impairment is a property of a transmission medium which causes the signal to be degraded, reduced in amplitude, distorted or contaminated.
Impairment can introduce errors into digital signals.
Examples of transmission impairments are attenuation, delay distortion, and several sources of noise including, thermal noise, impulse noise, and inter-modulation noise.

## Slide 152: Transmission Impairment

## Slide 153: Transmission Impairment
It is important to understand transmission impairments for several reasons.
Understanding the source of a transmission impairment like attenuation or dispersion will enable the user to partially correct for (equalize the signal) these effects.
Understanding the source of transmission impairments (dispersion, attenuation, impulse noise, thermal noise) can also help the user understand some of the constraints placed on the transmission of data as a result of these effects.

## Slide 154: Transmission Impairment
Such constraints include the maximum length of network links, the choice of physical transmission media, the choice of encoding methods, and the data rate supported by the medium.

## Slide 155: Transmission Impairment
Attenuation is a property of the transmission medium.
It measures how much energy is absorbed and/or radiated from the traveling signal due to it’s interaction with the transmission medium.
Attenuation is measured as a function of the distance traveled through the transmission medium.

## Slide 156: Transmission Impairment
The transmission medium absorbs energy because the signal is influenced by small impurities within it.
Such impurities have different sizes and distributions depending on the type of medium. Impurities of different sizes effect different frequencies in the signal.
The effect of attenuation is, therefore, a function of frequency.

## Slide 157: Transmission Impairment
The frequency variation of attenuation can be partially corrected, or equalized, by applying corrections based on a physical model.
When a signal is attenuated it’s amplitude is reduced.
The interpretation of a received signal depends on being able to tell the difference between different signal levels.
If the amplitude is reduced too much by attenuation it becomes impossible to accurately tell the difference between the different signal levels, and the information in the signal is lost.

## Slide 158: Transmission Impairment
To prevent this from happening repeaters (digital) or amplifiers (analog) are used.
These devices increase the amplitude of the signal by decoding and retransmitting the signal or increasing the received amplitudes respectively.
By inserting amplifiers or repeaters in the transmission media, the maximum signal propagation distance (a property of the attenuation of the medium) is increased.

## Slide 159: Attenuation

## Slide 160: Example
Imagine a signal travels through a transmission medium and its power is reduced to half. This means that P2 = 1/2 P1. In this case, the attenuation (loss of power) can be calculated as
Solution
10 log10 (P2/P1) = 10 log10 (0.5P1/P1) = 10 log10 (0.5) = 10(–0.3) = –3 dB

## Slide 161: Distortion

## Slide 162: Distortion
Dispersion is also a property of the transmission medium.
Signals with different frequencies will travel through a transmission medium with slightly different velocities.
Therefore, the signal will be smeared or distorted when it reaches the destination.
The longer the transmission medium the larger the time difference in the arrival times of the parts of the signal with different frequencies and the more severe the smearing or distortion of the signal.

## Slide 163: Distortion
Like attenuation, the physical properties of dispersion can be modeled.
Thus it is also possible to develop an equalization model to partially compensate for dispersion.

## Slide 164: Noise

## Slide 165: Noise
Noise of different types will affect a transmitting signal.
Thermal noise, low amplitude random noise at predictable low amplitude (amplitude related to the temperature of the transmission medium), is caused by the thermal vibration of the molecules within the transmission medium.
The difference between signal levels in a transmitted signal will generally be much larger than the amplitude of the thermal noise.

## Slide 166: Noise
Thermal noise sets a limit of how close different signal levels can be at the receiver (larger than the 2X amplitude of the thermal noise).
Thermal noise will not usually be of high enough amplitude to cause the introduction of bit errors in an encoded signal (unless attenuation has been excessive).
However, impulse noise picked up from the environment can have high amplitude for significant lengths of time

## Slide 167: Noise
Such impulse noise can be caused by interference from other signals in the environment including other transmitted signals, or electrical fields natural (lightning, aurora) or manmade (signals emitted by other electrical equipment).
The amplitude of impulse noise may reach or exceed the magnitude of the signal.

## Slide 168: Noise
The duration of a pulse of impulse noise may be several time the duration of a single signal.
Because of the large amplitude of the impulse noise pulse it is possible that, when added to the real signal, the resultant received signal may appear to have been transmitted at a different level that it actually was.

## Slide 169: Noise
For example,
for a signal with three levels (1 , 0, -1) and impulse noise has an amplitude of 1 added to a signal, the resulting received signal will have a level of (0, 1, 2).
During the noise pulse a signal transmitted at level 0 will arrive at the receiver with an amplitude of 1,.
Similarly a signal transmitted at level -1 will arrive at the receiver with an amplitude of 0. In both cases the level of the received signal will be different from the signal that was sent.
When the signal is decoded the resulting value of the data bit will have changed in transmission. A bit error has been introduced into the received signal.

## Slide 170: Signals
Throughput
Propagation Speed
Propagation Time
Wavelength

## Slide 171: Throughput

## Slide 172: Propagation Time

## Slide 173: Wave Length

## Slide 174: Signals
Digital Transmission

## Slide 175: Characterstics
Some Characteristics
Line Coding Schemes
Some Other Schemes

## Slide 176: Characterstics
The basis of analog signaling is a constant frequency signal known as a carrier signal, which is chosen to be compatible with the transmission media being used, so that it can traverse a long distance with minimum of attenuation and distortion.
Data can be transmitted using these carrier signals by a process called modulation, where one or more fundamental parameters of the carrier wave, i.e. amplitude, frequency and phase are being modulated by the source data.
The resulting signal, called modulated signal traverses the media, which is demodulated at the receiving end and the original signal is extracted.

## Slide 177: Characterstics
No of signal levels: This refers to the number values allowed in a signal, known as signal levels, to represent data.
Bit rate versus Baud rate:
The bit rate represents the number of bits sent per second, whereas the baud rate defines the number of signal elements per second in the signal.
Depending on the encoding technique used, baud rate may be more than or less than the data rate.

## Slide 178: Line Coding

## Slide 179: Signal Levels Vs Data level

## Slide 180: Digital Signal Encoding Formats

## Slide 181: Unipolar Encoding
In unipolar encoding technique, only one voltage levels are used.
It uses only one polarity of voltage level
Unfortunately, DC component present in the encoded signal and there is loss of synchronization for long sequences of 0’s and 1’s.
It is simple but obsolete.

## Slide 182: Unipolar Encoding
Unipolar encoding uses only one voltage level.
This scheme is very costly.
Unipolar scheme is normally not used in data communications today.

## Slide 183: Polar Encoding
Polar encoding uses two voltage levels (positive and negative).

## Slide 184: NRZ Encoding
Non Return to zero (NRZ):
The most common and easiest way to transmit digital signals is to use two different voltage levels for the two binary digits.
Usually a negative voltage is used to represent one binary value and a positive voltage to represent the other.
The data is encoded as the presence or absence of a signal transition at the beginning of the bit time.
As shown in the figure below, in NRZ encoding, the signal level remains same throughout the bit-period.
There are two encoding schemes in NRZ: NRZ-L and NRZ-I, as shown in Fig.

## Slide 185: NRZ Encoding

## Slide 186: NRZ Encoding
In NRZ-L the level of the signal is dependent upon the state of the bit.
In NRZ-I the signal is inverted if a 1 is encountered.

## Slide 187: Digital Transmission
The main problem with NRZ encoding occurs when the sender and receiver clocks are not synchronized. The receiver does not know when one bit has ended and the next bit is starting.
One solution is the RZ (return-to-zero) scheme, which uses three voltage levels.

## Slide 188: RZ Encoding

## Slide 189: RZ Encoding
Return to Zero RZ: Key characteristics of the RZ coding are:
Three levels
Good synchronization
Main limitation is the increase in bandwidth
The main disadvantage of RZ encoding is that it requires two signal changes to encode a bit and therefore occupies greater bandwidth.

## Slide 190: Manchaster
Biphase:
To overcome the limitations of NRZ encoding, biphase encoding techniques can be adopted.
Manchester and differential Manchester Coding are the two common Biphase techniques
In Manchester coding the mid-bit transition serves as a clocking mechanism and also as data.
In the standard Manchester coding there is a transition at the middle of each bit period.
A binary 1 corresponds to a low-to-high transition and a binary 0 to a high-to-low transition in the middle.

## Slide 191: Manchester
In Manchester encoding, the transition at the middle of the bit is used for both synchronization and bit representation.

## Slide 192: Differential Manchester
In differential Manchester encoding, the transition at the middle of the bit is used only for synchronization. The bit representation is defined by the inversion or noninversion at the beginning of the bit.

## Slide 193: Bipolar Encoding
In bipolar encoding, we use three levels: positive, zero, and negative.

## Slide 194: Sampling
Pulse Amplitude Modulation
Pulse Code Modulation
Sampling Rate: Nyquist Theorem
How Many Bits per Sample?
Bit Rate

## Slide 195: Modulation of Digital Data
Digital-to-Analog Conversion
Amplitude Shift Keying (ASK)
Frequency Shift Keying (FSK)
Phase Shift Keying (PSK)
Quadrature Amplitude Modulation

## Slide 196: Digital to Analog

## Slide 197: Digital to Analog

## Slide 198: Digital to Analog
Bit rate is the number of bits per second. Baud rate is the number of signal units per second. Baud rate is less than or equal to the bit rate.

## Slide 199: Digital to Analog
An analog signal carries 4 bits in each signal unit. If 1000 signal units are sent per second, find the baud rate and the bit rate
Solution
Baud rate = 1000 bauds per second (baud/s)
Bit rate = 1000 x 4 = 4000 bps

## Slide 200: Digital to Analog
The bit rate of a signal is 3000. If each signal unit carries 6 bits, what is the baud rate?
Solution
Baud rate = 3000 / 6 = 500 baud/s

## Slide 201: ASK

## Slide 202: FSK

## Slide 203: PSK

## Slide 204: PSK Constellation

## Slide 205: Analog Modulation

## Slide 206: Analog Modulation

## Slide 207: AM
The total bandwidth required for AM can be determined from the bandwidth of the audio signal: BWt = 2 x BWm.

## Slide 208: AM

## Slide 209: Frequency Modulation

## Slide 210: Sampling
Analog data such as voice, video and music can be converted into digital signal communication through transmission media. This allows the use of modern digital transmission and switching equipment’s. The device used for conversion of analog data to digital signal and vice versa is called a coder (coder-decoder). There are two basic approaches:
Pulse Code Modulation (PCM)
Delta Modulation (DM)

## Slide 211: Sampling
Pulse Code Modulation involves the following three basic steps as shown in Fig. :
Sampling – PAM
Quantization
Line coding

## Slide 212: Sampling

## Slide 213: Sampling
Sampling: This process is based on Shannon’s sampling theorem. Numbers of samples of the signal are taken at regular intervals, at a rate higher than twice the highest significant signal frequency. This basic step is known as Pulse Amplitude Modulation (PAM) as shown in Fig. . For example, during the sampling of voice data, in the frequency range 300 to 4000 Hz, 8000 samples per second are sufficient for the coding

## Slide 214: Sampling

## Slide 215: PAM
Pulse amplitude modulation has some applications, but it is not used by itself in data communication. However, it is the first step in another very popular conversion method called pulse code modulation.

## Slide 216: PAM

## Slide 217: PCM

## Slide 218: Analog to PCM Digital code

## Slide 219: Analog to PCM Digital code

## Slide 220: Sampling
According to the Nyquist theorem, the sampling rate must be at least 2 times the highest frequency.

## Slide 221: Example
What sampling rate is needed for a signal with a bandwidth of 10,000 Hz (1000 to 11,000 Hz)?
Solution
The sampling rate must be twice the highest frequency in the signal:
Sampling rate = 2 x (11,000) = 22,000 samples/s

## Slide 222: Example
We want to digitize the human voice. What is the bit rate, assuming 8 bits per sample?
Solution
The human voice normally contains frequencies from 0 to 4000 Hz.
Sampling rate = 4000 x 2 = 8000 samples/s
Bit rate = sampling rate x number of bits per sample = 8000 x 8 = 64,000 bps = 64 Kbps

## Slide 223: Example
We want to digitize the human voice. What is the bit rate, assuming 8 bits per sample?
Solution
The human voice normally contains frequencies from 0 to 4000 Hz.
Sampling rate = 4000 x 2 = 8000 samples/s
Bit rate = sampling rate x number of bits per sample = 8000 x 8 = 64,000 bps = 64 Kbps

## Slide 224: Sampling
Delta Modulation (DM)
Delta Modulation is a very popular alternative of PCM with much reduced complexity.
Here the analog input is approximated by a staircase function, which moves up or down by one quantization level (a constant amount) at each sampling interval.
Each sample delta modulation process can be represented by a single binary digit, which makes it more efficient than the PCM technique.

## Slide 225: Sampling
In this modulation technique, instead of sending the entire encoding of each and every sample, we just send the change from previous sample.
If the difference between analog input and the feedback signal is positive, then encoded output is 1, otherwise it is 0. So, only one bit is to be sent per sample.

## Slide 226
Multiplexing

## Slide 227
Dividing a link into channels

## Slide 228
Frequency-division multiplexing

## Slide 229
FDM is an analog multiplexing technique that combines analog signals.
Note

## Slide 230
FDM process

## Slide 231
Wavelength-division multiplexing
Notes: IT’S A PRISM NOT THE MUX HERE

## Slide 232
TDM

## Slide 233
TDM is a digital multiplexing technique for combining several low-rate channels into one high-rate one.
Note
Cont …

## Slide 234
Synchronous Time-Division Multiplexing

## Slide 235
Telephone System
Notes: 5 main components: end device, local loop, trunck, local office/tandom office and reginal office

## Slide 236
Telephone System

## Slide 237
Telephone System

## Slide 238: Review Questions (Short)
What is computer networking? Discuss the various types of it.
Give the names of various layers in OSI model. State the role of network layer in it.
What do you mean by wireless transmission? Briefly describe the various media that support wireless transmission.
Distinguish between FSK, PSK and ASK? Discuss Pulse code modulation.

## Slide 239: Review Questions (Long)
An analog signal has a bandwidth of 40 KHz. If we sample this signal and send it through a 50Kbps channel. What is the SNR?
Which of the four digital-to-analog conversion techniques (ASK, FSK, PSK or QAM) is the most susceptible to noise? Defend your answer.
Explain Mobile Telephone System.
Difference between guided and unguided media with the help of an example.
Explain Pulse Code Modulation.
What does the Shannon capacity and Nyquist theorem have to do with communication?

## Slide 240: Recommended Reading
Behrouz Forouzun, “Data Communication and Networking”:TMH
Tanenbaum , “A computer Networks”: Prentice Hall
Stallings , “High speed Networks” :Prentice Hall
Comer D. “Computer Networks”: Prentice hall
Kurose, J and Ross , “Computer Networking : Addison Wesley